## Slide 1: Sustainable Materials Management: Using Lifecycle Thinking for Strategic Goal Setting
WDOE
October 4, 2017

## Slide 2: The State of Recycling Goals
States, cities and corporations have developed aspirational diversion goals: 50%, 75%, 100%
Weight-based recycling has been our measure of material management performance
Cities added more materials and convenient programs to help achieve their goals.
Do we have the right goals?
Notes: Let’s start by looking back to the early years of recycling, when the amount of material that we recycled was the metric that we had to measure the success of perhaps one our most visible environmental programs. We knew recycling was good. And if recycling was good, then recycling more must be a better. Right?
We’ve been so focused on recycling everything for so long it has become the proxy for the environmental. – in some cases forgetting why we recycle in the first place. Have we lost sight of what the real goal is, which is to improve the outcomes?
As we’ve learned more about lifecycle analysis, and the concepts of sustainable materials we’ve started to ask different questions:
- How do we achieve the best environmental benefits?
- How do we prioritize our efforts?
- How do we measure our success?
- What should our goals be?

## Slide 3: The Evolution of an Industry
Many of the materials that have been added to recycling programs have increased recycling processing costs, or are hard (impossible) to market
As the waste stream has changed, it has become more complex and contamination has increased
Achieving weight based goals will become even more difficult and expensive with China’s new policies on material bans.
We have more data in 2017 to help define environmental outcomes.
Notes: These questions force us to think about changes in our industry and in society.
We live differently and we purchase differently. More on the go lifestyles means that we purchase products to meet this lifestyle
Products and packaging have evolved. They always have and always will…. But we now find that many of the new packaging is not recyclable, even though it may have net environmental benefits. Unfortunately, we don’t always have a good way to measure this net impact….
As the waste stream becomes more complex, contamination has increased, which increases the cost of recycling
China’s pending materials ban combine with low energy prices in the U.S. may force us to make new decisions based on markets and cost. With a renewed focus on quality as materials compete for end markets, education and processing costs may increase recycling cost in a period of volatile markets..

## Slide 4
What we recycle now
Notes: Many of you have seen a variation of this chart before. The red bars on the left are those types of packaging that have been declining in prevalence since 1990, and the green on the right are those that are increasing.
This chart that shows how much of each packaging material type we are recycling. Most of what we are currently recycling is the stuff that we are using less of…. Other than cardboard, we are using more of the things with the lowest recycling rates (and the things that weight less).
No wonder we are having a hard time growing recycling! And – its only going to get harder!

## Slide 5: Packaging Peaked in 2000
Per capita packaging generation has fallen from 0.27 tons per person annually in 2000 to less than 0.24 tons in 2013
Per capita packaging is roughly equivalent to 1983 levels.
Courtesy: SPC
Notes: This slide is from the Sustainable Packaging Coalition.
As you can see, packaging generation peaked in the year 2000, and has been declining since. We pay attention to this since most material in curbside recycling programs is packaging. Even with the rebound following the economic downturn, Per capita packaging generation has fallen from 0.27 tons per person annually in 2000 to less than 0.24 tons in 2013, having trended downward steadily since 2009 and roughly equivalent to 1983 levels.
Packaging will continue to become more efficient, which is encouraging, however it makes it harder to increase our recycling rate. We are sort of swimming upstream as changes to the waste stream and global recycling conditions make it harder to improve our recycling rates.

## Slide 6: Paradigm Shift: From Weight to Environmental Burden
o
Is our goal to recycle more tons?
Or reduce environmental impact?
The goal is to reduce environmental impacts.
Recycling is one way to achieve the goal.
Reduction is a better way to achieve the goal.
Notes: Which bring us to our discussion today around whether it is time for a paradigm shift.
For decades, we've used recycling as a proxy for environmental good, and have focused on recycling more tons in order to reach weight based recycling goals.
Based on EPA’s work on SMM, we are asking if it’s time to evolve and think differently, and to focus goals that consider lifecycle thinking to look at broader environmental benefits rather than arbitrary end-of-life weight-based goals that take the focus away from the real reason why we reduce, reuse and recycle in the first place.

## Slide 7
Limitations of Optimizing “Solid Waste”
2006 U.S. GHG inventory
with 32% recovery
(MSW)
2006 U.S. GHG inventory with
very high recovery rate
(~95% MSW + >70% C&D)
42%
Provision of
materials
Provision of
materials
36%
Savings=6%
Buildings
Transporting
people
Appliances
& devices
Buildings
Transporting
people
Appliances
& devices
Notes: I’m sure that many of you have seen the pie chart on the left, which shows our nation’s domestic greenhouse gas emissions organized by economic system. In this “systems-based inventory” the provision of materials contributes 42% of our nation’s greenhouse gases – more than the operation of buildings, and more than transporting people.
But on the right you’ll see that if we could achieve exceptionally high recovery rates (95% of all municipal solid waste and about 70% of all construction and demolition debris), the reduction in emissions would be meaningful, but still only about 6%, leaving most of the emissions untouched.
Greenhouse gases are only one example, but if we want to use materials in a manner that is environmentally and economically sustainable, we’re going to need some additional approaches. And that’s what sustainable materials management provides us, is a bigger toolbox.
I want to repeat here that the overarching goal is to conserve resources and reduce pollution. While the goal is no longer just landfill diversion or high recycling rates, they absolutely can help to achieve these higher goals.

## Slide 8: A Tale of Two States: Oregon and Florida
Oregon: ODEQ is in the process of implementing new reduction goals based on Sustainable Materials Management
Florida: University of Florida is driving a review of the State’s 75% recycling goal and reframing in terms of Sustainable Materials Management
Notes: This all makes sense, right? But I am pretty impressed at how hard it is to change. I hear time and time again that it’s too hard to change. Weight is so easy to grasp and measure, it’s hard to envision another system that we could move towards.
Fortunately, we have some examples that we can use to demystify this:
First – Of course we will look at Oregon. The work that they are doing is very good, and it is replicable.
Then, I’ve included some information from University of Florida professor Dr. Tim Townsend. His team at The Hinkley Center at the University of Florida has suggested that we reduce the environmental burden, as he calls it, of materials and programs. One thought coming out of Florida is the idea of switching from their 75% recycling goal to a 75% emissions reduction goal. We’ll touch on what might look like.

## Slide 9: Oregon Material Flow Approach
Focuses on the environmental outcomes of waste management
Uses life cycle analysis of the materials in Oregon’s waste stream
  Full life cycle, not only end-of-life
  Ultimately will incorporate demand, not just waste
Supports more and better recycling and waste prevention
Notes: Oregon’s work focuses on the environmental outcomes of waste management
They use life cycle analysis of the materials in Oregon’s waste stream
  Full life cycle, not only end-of-life
  Ultimately will incorporate demand, not just waste
Supports more and better recycling and waste prevention
I think we all can benefit from the work Oregon is doing. And - they are looking to find ways to share it.
I have a few slides that highlight their efforts.

## Slide 10: Limits to Weight Based Recovery Goals
All recovery is the same (recycling = composting = energy recovery*)
All materials are the same (aluminum = yard debris)
All end-markets are the same (glass to bottles = glass to roadbed)
Encourages “recovery for the sake of recovery”
Some energy recovery is excluded
Does nothing to move up the hierarchy, no value to reduction or broader lifecycle thinking.
* For illustrative purposes. States count energy recovery differently.
Notes: At the heart of their effort is a discussion of the limitations of weight-based recycling goals. Here are a few shortcomings, as noted by David Allaway from Oregon’s DEQ:
With weight based goals:
All recovery is the same (recycling = composting = energy recovery)
All materials are the same (aluminum = yard debris)
All end-markets are the same (glass to bottles = glass to fill)
Encourages “recovery for the sake of recovery”
Some energy recovery is excluded
Does nothing to move up the hierarchy, no value to reduction or broader lifecycle thinking.
So the next obvious question is – how can we address these shortcomings with our current system of weight-based goals?
While we will always need weight to measure our progress, we can create strategic goals that target environmental benefits by looking differently at the materials we manage.

## Slide 11: Weight based recovery measurement
Chart: 
| Aluminum Cans | Mixed Paper (general) | Corrugated Containers | Steel Cans | Newspaper | PET | Mixed Plastics | HDPE | Glass | Carpet
Series 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Tons
Notes: This slide represents the recovery of 1 ton of each of the materials in the graph. As the folks in Oregon point out, it’s not very useful….. But it’s pretty much what we see now when we talk about weight-based recycling goals. We’re just counting tons. Since goals are based on weight we are completely ignoring the fact that recovering different materials have different benefits.
Think about it. Why do we recover materials for recycling? Recycling reduces the upstream energy and pollution caused by mining virgin materials to make products. However, the varying environmental benefits of recovering each of these materials are not addressed in any of our existing goals.
So, what are the environmental outcomes of recycling the materials in this chart?

## Slide 12
Chart: 
| Aluminum Cans | Mixed Paper (general) | Corrugated Containers | Steel Cans | Newspaper | PET | Mixed Plastics | HDPE | Glass | Carpet
Series 1 | 9.1 | 3.5 | 3.1 | 1.8 | 2.7 | 1.1 | 1 | 0.9 | 0.3 | 2.4
GHG Impact of One Ton of Recycled Material
MTCO2e
Notes: As you can see there are huge differences! Information like this can help us target the materials that reap the biggest environmental benefits.

## Slide 13: Material Specific Recovery Goals
25% recovery by 2025
25% reduction by 2020
25% recovery by 2020
Notes: Using lifecycle analysis of the actual materials in their waste stream, Oregon created outcome based material recovery goals that target specific materials based on environmental impact.
This slide is an example of the goals that Oregon has established for carpet, food and plastics based on science.
The goals were created after looking at GHG emission reduction potential and other environmental attributes.
Where does the cost of recovery efforts enter this picture? Setting recovery goals based on environmental attributes doesn’t consider economics. Some say that is a shortcoming with LCA, but I think they are two very separate discussion.
Each material type will need a unique analysis - which is a key point to this effort.

## Slide 14: Implementing Oregon’s 25% Food Reduction Goal
In 2017, Oregon released their plan to achieve their 25% food reduction goal.
1. Wasted Food Measurement Study | 6. Edible Food Rescue
Messaging | 7. Labelling
3. Consumer Outreach | 8. Coalition of Interested Regional Parties
4. Schools | 9. Research Not included elsewhere
5. Commercial Sector | 10. Guiding Principles for Project implementation
The plan identifies key priorities focusing on upstream prevention and recovery, instead of end-of-life:
Preventing one ton of food from being wasted results in 6X larger lifecycle GHG benefits than composting, and 7X the GHG emission benefits of anaerobic digestion
Their plan focuses solely on upstream prevention and recovery – rather than EOL recycling.
Notes: Once material specific goals have been established, programs for achieving them can be developed.
Earlier this year, Oregon released its Food Reduction Plan. The lays out 10 priority programs to achieve the state’s 25% Food Reduction goals.
Oregon’s Food Recovery plan is remarkable for its approach to achieving the state's goal.
Recognizing that preventing one ton of food from being wasted results in 6 times larger lifecycle GHG benefits than recycling one ton of food through composting, and 7 times the GHG emission benefits of anaerobic digestion, their plan focuses solely on upstream prevention and recovery – rather than EOL recycling.

## Slide 15
Recycled Content Doesn’t Consistently Predict Environmental “Goodness”
Example: Concrete
44% recycled content (aggregate)
8% recycled content
(slag)
Chart: kg CO2e
| Mix 1 | Mix 2 | Mix 3
kg CO2e | 292 | 283 | 191
44% recycled content (aggregate)
8% recycled content
(slag)
0% recycled content
Notes: Here’s another example from Oregon about how this SMM view plays out.
Local governments wanting to advance recycling often encourage purchasing agents to maximize the recycled content of the stuff they buy. And while this often reduces environmental impacts, it isn’t always the best approach.
First column: Consider concrete, a material that has a huge carbon footprint and that governments buy a lot of. This graph shows the carbon footprint of a cubic yard of concrete with no recycled concrete in the Pacific Northwest.
Concrete is a mixture of water, aggregate, sand and cement. It is mostly aggregate so recycled content can be maximized by specifying recycled aggregate.
Second column: And here’s the carbon footprint of that concrete, with 44% recycled content: the carbon footprint is hardly lower. And the reason is: the carbon footprint of concrete is dominated by cement. And some of that cement can often times be replaced with other materials, such as fly ash, or steel slag.
The third mix, that has only 8% recycled content – in the form of steel slag – but the carbon footprint is 34% lower.

## Slide 16: The Florida Story: Academics at Work
The University of Florida project was driven by an interest in material measurement and impact. Materials counted have changed over the past two decades
Recognition of the role of SMM and Lifecycle Assessment
State-wide workshops now contemplating how to apply this information to the State’s 75% goal.
Florida’s Recycling Rate
Notes: Now, let’s switch gears, and move diagonally across the country to Florida, with its current 75% recycling goal. Florida isn’t exactly a bastion of environmental thinking (ie their recycling goal includes WTE).
However, work being done at the University of Florida is similar to that in Oregon, but they are going about it very differently. Rather than the State driving the change, the University of Florida has completed some analysis that is driving change. Not as sophisticated as Oregon’s work but they’ve developed some helpful examples.
Dr. Tim Townsend, at the University of Florida started thinking about
their weight based system about two years ago, and the environmental impact of the various materials in the waste stream.
Over the years, the State of Florida has added and subtracted materials from their inventory: they took C&D out of their MSW counting inventory in 1998, then added WTE tons as recycling in 2010.
Recognizing the impact of these changes to tons, Dr Townsend looked at other cities in the US and Germany to see the impact there on their recycling rate. Indeed, much of San Francisco’s 80% recovery rates comes from counting inert materials and biosolids.
This set him down a path to think about the environmental impacts of various types of materials rather than just tons diverted.

## Slide 17: 1: Waste Characterization
Sarasota County
Notes: Dr. Townsend’s process closely mirror that in Oregon
Dr. Townsend started by looking at the waste characterizations of several counties in the Florida.
Here is one example – Sarasota County, a high performing county in Florida.

## Slide 18: 2. Evaluate Environmental Impacts
Greenhouse Gas Emissions
Energy
INPUTS: Materials by disposition (tons)
Impact factors (by material & disposition & life cycle stage)
OUTPUT: Impact of each material type
Notes: Next, using the tons for each type of material, he created a GHG emissions impact by material types. He also looked at the energy reduction potential for each material.
These chart list each type of material in the waste characterization study. It uses the environmental impact of a ton of each type of material multiplied by the number of tons of each to look at the relative environmental burden of each type of material in the waste stream.
From a GHG emission perspective, C&D, Metal and Paper are areas focus on to reduce GHG emissions.
And from an energy perspective, reducing metals, paper and plastic bottles would reduce energy use the most.
This is a function of both the impact per ton as well as the number of tons in the stream.
The equation at the bottom is from Oregon. You can see the similar line of thinking

## Slide 19: 3. Setting New Goals
University of Florida recommends using a Base Year to create an “Environmental Burden Baseline”
Create a target reduction goal from this number
The University of Florida introduced the idea of replacing their 75% recycling goal with a 75% GHG emissions reduction goal.
Notes: Armed with this data, the University of Florida team has proposed that the state use their 2008 goal setting year as their base year. They determined the environmental burden for that year using the number of tons of each material types times the GHG emissions or energy used for each material.
They are suggesting that the State create a 75% emissions or energy reduction goal from this total – rather than a 75% recycling goal.
Then, the state can develop programs to achieve these goals, prioritizing those material that will get them to their goal, based on their material-specific analysis.
This is a variation of Oregon’s specific material goals, but it uses material specific goals to achieve their environmental burden reduction goals.
This is simply smart goals setting, using real data. And, it’s appropriate for 2017!
Use Base Year outputs to create an “Environmental Burden Baseline”
Create a target reduction goal from this number
The University of Florida is recommending a 75% GHG emissions or Energy emission reduction goal from the baseline, instead of an overall 75% recycling goal.

## Slide 20: 4. Develop Programs to Achieve the Goal
2015 Traditional Recyclables
With WTE
80% Cans &and Bottles
80% of Paper
Food
Waste
C&D, Yard Waste
What 75% GHG Emissions Reduction Looks Like
Total
Notes: I included this chart which is one example of programs that could be developed to achieve a 75% GHG emissions reduction goal. The point is that the work done by Oregon, Florida and WM (next example) was done separately and get to the same conclusion. Focus on recycling the right things to maximize environmental benefits. And, as Oregon has done – look bigger. Consider reduction and reuse along the lifecycle of material production, use and EOL disposition.
The state of Florida could exceed their 75% GHG emissions reduction goal by focusing on recycling the bottles, cans and paper in the waste stream really well. If they captured 80% of the “basics” they would achieve their 75% recycling goal.
Food, C&D and Yard Waste will absolutely add more benefits, but they can’t get you there alone.
Dr Townsend and his team looked a variety of different programs and scenarios for achieving a 75% GHG Emissions reduction goal. This is just one of their scenarios.
The point is that it is based on real data about environmental benefits, and programs can vary by community and by different community’s priorities for how to achieve the overall emissions reduction goals.

## Slide 21: Florida Lessons Learned
Different recycling approaches result in different progress towards the goal
The type of materials targeted makes a difference
The selection of a baseline is critical
Notes: Key takeaways from the Florida example:
Different recycling approaches result in different progress towards the goal
The type of materials targeted makes a difference
The selection of a baseline is critical.

## Slide 22
Scenarios build upon each other
84% GHG benefit from aggressive LFG capture & use + recycling 32% of MSW
More processing = high incremental cost for low incremental GHG reduction
84% of GHG reduction benefit from 32% diversion through Residential & Commercial SS Recycling
WM Spectrum: What we found
Notes: Main point of slide: 84% of GHG reduction benefit from 32% diversion through Residential & Commercial SS Recycling (Spectrum basis of 214M tons, not all EPA 2013 MSW tons)
Recycling, followed by LFG Capture & Use makes up the bulk of the potential GHG emissions reductions
Collection GHG impact negligible even with separate collection of organics & recycling using all diesel trucks
  NOTE: we did not evaluate the financial profitability of Natural Gas trucks – that was outside the scope of this analysis. Natural Gas trucks may make financial sense on their own, plus other emissions factors (SOx, NOx, particulates, etc.) may be a bigger factor.
TO DISCUSS: We should revisit collections at some point. Underlying assumption is non-overlapping fleets in an area. This is probably right for municipal contracts, however it likely understates commercial open-market service GHG impacts. Likely still negligible, but more than we currently show.

## Slide 23
  GHG impact from collection is negligible. NGV trucks reduces collection GHG impact 20%, but off small base
Greatest GHG benefits from recycling
Above x-axis = emissions reductions
Recycling is bulk of the potential GHG emissions reductions
Notes: Main point of slide:
Colors below the x axis are emissions, bars above x axis are emissions reductions.
Recycling makes up the bulk of the potential GHG emissions reductions
Collection GHG impact negligible even with separate collection of organics & recycling
Emissions reductions are primarily the result of reduced GHG emissions associated with less mining/use of raw resources NOT the impact at the landfill (even more true in v14)
Background
NGV trucks reduce collection GHG impact 20%, but off small base
Compost: YW in EPA WARM = (grass, leaves, branches). Grass anaerobically degrades & releases methane quickly in LF; in WARM, leaves & branches never degrade & sequester carbon
Updates to WARM forthcoming – part of our recommendations for next steps
WTE: planning to analyze next
Collections excludes: Off-road equipment, delivery of commodity recyclables (b/c included in “recycling”)

## Slide 24
Not all organics are created equal:
  Foodwaste has greatest emission reduction potential, grass is next.
  Leaves and branches have least emissions in Best Practices landfill (EPA)
Mixed Organics in EPA’s Warm Model averages all blends of organics:
  YW = grass, leaves & branches. FW = all FW, including produce, diary, meats
  Mixed Organics =
  48% Yard Trimmings + 52% Food Waste
  Yard Trimmings =
  25% Leaves + 25% Branches + 50% Grass
Notes: COMPOST: In WARM, yardwaste composting emits more MTCO2e than Landfill. However:
Foodwaste composting emits much less MTCO2e than landfill
Foodwaste composting requires Yardwaste in the process - can’t just compost Foodwaste
WARM does not capture fertilizer value (N, P, K) of compost (However, this may be very small)
Data & Methodology for Yardwaste composting in WARM may be old; updates likely in future versions of WARM
Background:
Red line also shows relationship to volume
Mixed Organics = 52% Food Waste, 48% Yard Trimmings
Yard Trimmings = 50% grass, 25% leaves, 25% branches

## Slide 25
Collections is 70-80% of integrated costs until post processing options
Infrastructure cost of new technologies is very high
Commodity revenue is based on 10-year average blended value
Collections = 70-80% of cost with traditional disposal & recycling services
Processing costs become significant for waste conversion technologies
Notes: Main point of slide
Now we switch to cost. Collection is 70%+ of cost until we get to the conversion technology scenarios with high infrastructure.
Background/other:
Product sales averaged over all 213M Tons even though recycling only 34M tons. $87.90 Blended Value per ton assumed for all recycling.
Technologies: Conversion technologies include gasification (ie Enerkem) or pyrolysis (Agilyx)

## Slide 26
Costs plus environmental benefits create a single metric = $/ton of GHG
Width of bars is GHG reduction, height is cost of GHG reduction
Also includes LCFS & EPA social cost of carbon as proxies
LFGTE, Residential & Commercial Single-Stream Recycling are more cost-effective options for reducing GHG emissions
Conversion technologies are less cost-effective methods for reducing GHG emissions
Notes: Assumes 10 year average commodity prices
Purpose of Graph
  This slide uses the costs & environmental benefits calculated thus far to create a single metric: cost per metric ton of GHG reduction. This is the incremental cost required to achieve a metric ton of GHG reduction
  The width of each bar is the GHG emissions reduction and the height is the cost.
  This enables us to understand and prioritize our strategies.
  On this basis, the most Environmentally Profitable strategies are LFGTE, Residential & Commercial Recycling
  Conversion Technologies are less cost-effective methods for reducing GHG reduction
Education tool for Customers:
  The model illustrates the environmental value of various solid waste strategies
  Customers who care about GHG emissions should be prepared to pay premiums in order to achieve GHG reduction targets.
  One example: Oregon is using the EPA Social Cost of Carbon calculations in their planning process. We’ve gone over this model with them – very similar to their work.
Opportunity to educate our customers:
  Is weight based recycling % the right goal? No – we think GHG reduction is the goal, however it is too abstract for regulators & customers.
  This analysis gives us a tactical tool to enable our customers to achieve create & execute economically-efficient environmental goals & talking points to help us negotiate existing contracts.
  For example: there’s a logical order to maximize GHG reduction while minimizing the financial cost
Background
  Don’t do Conversion Technologies without robust Organics & Recycling
  Organics: somewhere in the middle…FW vs YW…
  Scenario 6d: 276 Million MTCO2e reduction (4.2% US GHG budget)
  $10 per MTCO2e equates to $26/ton Blended Value
  EPA Social Cost of carbon: 3% discount rate, 95% percentile represents a “higher-than-expected” estimates for the Social Cost of Carbon
NOTES:
Abatement curves assume PRICE, not COST. Margins assumptions in appendix
Links:
EPA Social Cost of Carbon: http://www3.epa.gov/climatechange/EPAactivities/economics/scc.html
CA LCFS Credit Price: http://www.arb.ca.gov/fuels/lcfs/credit/20151013_sepcreditreport.pdf
GHG Abatement curves, see: http://www.mckinsey.com/client_service/sustainability/latest_thinking/greenhouse_gas_abatement_cost_curves
For more information on GHG Abatement curves, see: http://www.mckinsey.com/client_service/sustainability/latest_thinking/greenhouse_gas_abatement_cost_curves
Other industry metrics:
Gasoline: $1/MTCO2e = $0.01 per gallon. Therefore, $100/MTCO2e = $1.00/gallon
Electricity: $1/MTCO2e = $0.001/kWh. Therefore, $100/MTCO2e = $0.10/kWh
If society had to pay a $1/gallon or $0.10/kWh “tax”, hybrids & rooftop solar would be standard across the country…without any additional incentive.
One argument: Why should society pay even more for Waste Conversion processes in order to achieve relatively modest reductions in GHG when not doing so elewhere?

## Slide 27
Environmental benefits & cost per ton of carbon reduction for recycling only
Includes collection, processing and commodity values
Results show the benefits of recycling paper, metal and plastic bottles
Notes: Main point of this slide
This is the same basic concept, but instead of scenarios it looks at commodities in our recycling program
We looked at the cost (or benefit) of recycling these commodities, including collection, the processing and marketing . We applied the economic value to the per ton GHG emissions reduction impact to depict the cost per ton of carbon emission reduction for every ton of each materials
Recycle paper, metal, PET, HDPE all day long
Recycling one ton of metal results in 3.94 MMT C02 emission reduction at an positive economic value.
For plastics, one ton recycled results in 1.1 MMT C02 reduction at an economics value.
For paper – barely…
And for glass –one ton of glass recycled results in 0.32 MM tons of Carbon reduced, but it comes with a net cost.
Background
Graph
  Profitable commodities are above the line, unprofitable commodities above the line
  Logical order of materials to recycle based on Economics & GHG reduction potential
  Some commodities are valuable + easy & cheap to separate (Aluminum Cans)
Commodity prices
  Used 10 year historical analysis b/c not getting accurate assessment from snapshot in time (same as whole market areas)
  Commodity price assumption drives which commodities make sense, but does not change magnitude of profitable GHG reduction potential
Processing costs
  Used WM processing cost assessment by commodity. Difficult to assess, but comfortable that we are directionally correct.
  Includes cost of recycling collection & avoided MSW disposal
  Does not include impact on MSW collection (tons down & cost down, but cost/ton up)
  SUSAN: Do we want to keep this slide as “Benefit” (Steiner’s original request) or switch to “Cost” (more in line with previous graph & typical GHG abatement curves found elsewhere)?

## Slide 28
MRF feedstock increased by 15% over the past decade
Cost increased by 63% (adjusted for inflation)
Analysis indicates that 7 materials caused the increased cost with negligible contribution to recycling: Gable Top Cartons, Aseptic Containers, Paper Laminates, Plastic Film, Plastic Laminates, Polystyrene and Other Plastics.
Ontario Materials Study
Notes: Work by York University in Ontario
MRF feedstock increased by 15% over the past decade
Cost increased by 63% (adjusted for inflation)
Analysis indicates that 7 materials caused the increased cost with negligible contribution to recycling: Gable Top Cartons, Aseptic Containers, Paper Laminates, Plastic Film, Plastic Laminates, Polystyrene and Other Plastics.
The point of this slide is that recycling “Core” materials in curbside recycling programs offers the greatest environmental benefit at the least cost. Similar to WM’s Spectrum – it offers a prioritization of programs. Fringe materials, as they are called by ASTRYX/SPC/TRP add cost with little environmental benefit.

## Slide 29
37
Chart: 
Chart: 
| Cardboard | Glass | Mixed Plastics | Mixed Paper | Mixed Metals | Food Waste | Mixed MSW
 | 0.035892 | 0.13773 | 0.054186 | 0.049088 | 0.041567 | 0.26411 | 0.417
Cardboard
Mixed Plastics
Mixed Metals
Glass
Mixed
Paper
Scenario | Baseline | Source Separated | Mixed Recyclables | Foodwaste added
Mixed waste |  |  |  | 
Foodwaste |  |  |  | 
Glass |  |  |  | 
Mixed Recyclables |  |  |  | 
Cardboard |  |  |  | 
Cost/ton | $42/ton | $35/ton | $40/ton | $55/ton
Weight
GHG Emissions
Commercial Generator
Notes: Here is an example of how we can use lifecycle thinking to evaluate goals and programs.
This is one large commercial customer - a hotel, with a lot of food.
The pie chart on the left is their tons, and you can see that about 25% of the tons they generate are food.
The chart on the right is the GHG emission reduction potential associated with recycling their waste stream. Because of the relatively large amount of food in their waste stream, we were all surprised to learn that they can still capture the vast majority of their emissions benefits by recycling traditional recyclables. Emissions from food are a relatively small portion of their overall inventory, but would add significant cost.
This generator immediately got the point of this analysis. They identified their opportunity to focus their limited dollars on recycling traditional recyclables really well - but also, to reduce their food waste. Then, as they maximize their other programs, they can tackle the remaining food in their waste stream for recycling for an overall maximum environmental benefit.

## Slide 30
Step 1:
Waste Characterization
Complete state-wide waste characterization study of disposed materials
Step 2:
Evaluate Environmental Impact
Use waste characterization and LCA to prioritize goals based on environmental benefits
Step 3:
Set Goals
Develop material specific waste reduction & recovery goals to maximize environmental benefit
Step 4:
Develop Programs and Measure in tons
Convert goals to tons to measure reduction and recovery.
Developing goals and measuring success
Notes: Here is what we think the process looks like in this new way of thinking
Step #1: Evaluated all tons
Waste Composition Study
Step #2: Estimated “environmental impact(s)” of these materials across their life cycle
Environmental impacts = energy + others (GHGe, toxicity, other)
Benefits of recovery by material, recovery pathway, and end market
Magnitude of these benefits relative to “big picture” – Look at full life cycle of waste generation
Step #3: Set the goals. Based on the areas they’ve identified as having the greatest opportunity to reduce environmental impact, they’ve set material specific goals.
Step #4: Finally, use the material specific information to develop programs to meet the goals. Then, measure progress using annual tonnage reporting and periodic waste characterization studies! Need to consider per capita reduction from a base year to capture reduction, rather than just diversion.

## Slide 31: Summary
It’s time to think differently about how we set goals for materials management
Focus on individual materials. Using data lets us be strategic in maximizing broader environmental benefits.
Lifecycle thinking lets us prioritize programs for the best overall environmental results
Emphasize material specific goals. After developing material specific goals, per capita reduction (measured in tons) allows us to measure from a base year.
Policies should focus on the primary goal:
Reducing overall environmental impact
Notes: It’s time to think differently about how we set goals for materials management
We have data to be strategic - maximizing broader environmental benefits by focusing on individual material types
Lifecycle thinking lets us prioritizing programs for the best overall environmental results.
We can still use tons….. Per capita reduction is measured by tons.
That’s it. Thanks so much. I’m happy to answer your questions.

## Slide 32: Thank you!

## Slide 33: Measuring Success: US EPA
Chart: Material Landfilled
| Paper and Paperboard | Glass | Ferrous Metals | Aluminum | Other Nonferrous Metals | Plastics | Rubber and Leather | Textiles | Wood | Food | Yard Trimmings
Landfilled | 19470 | 7040 | 9830 | 2360 | 630 | 25100 | 4150 | 10460 | 11010 | 29310 | 10790
Chart: 
| Paper and paperboard | Glass | Steel | Aluminum | Other nonferrous metals | Plastics | Rubber and Leather | Textiles | Wood | Food, Other | Yard trimmings
GHG emissions/ton recycled | 3.1174 | 0.27652 | 1.8123 | 9.1078 | 4.3404 | 1.0002 | 0.37616 | 2.358 | 2.4616 | 0.17601 | 0.14631