## Slide 1
Waste to Energy Evaluations
Jamey Barker
January 22, 2020

## Slide 2
King County Has Studied Evolving Waste Technologies for 40 years.
1980s
Energy Recovery Program
2008
Alternative Disposal Technologies
2017
Advanced Material Recovery & Waste To Energy (SWD)
2018
Waste To Energy (Normandeau)
2019
Waste To Energy vs. Waste Export by Rail (ARCADIS)

## Slide 3
Background Assumptions
King County will reach zero waste of resources.
Recycling lowers disposal costs and increases carbon offsets.
WTE technology would be MSW mass burn.
WTE doesn’t produce recognizable renewable energy.
4,000 TPD of disposal capacity for the next 20 yrs.
EPA’s WARM model is the tool for evaluating GHG

## Slide 4
WTE Financials
Initial capital costs estimated at $1.4 B - $1.8B
Additional capital costs required for future expansion (10-15 yrs.)
Energy sales offset costs, however;
  Difficult to forecast
  Future value depends of Clean Energy Transformation Act
  Washington power pricing is relatively low

## Slide 5
New State Laws Increase Challenges/Costs for WTE
By 2030 utility generation will need to be carbon neutral
By 2045 utility generation will be non-emitting
Technology to make WTE non-emitting has not been proven feasible at this scale
Energy revenue offsets approximately $30M/year for a 4,000 TPD plant.

## Slide 6
For King County, Further Development of Cedar Hills Was the Right Choice for 2028
COMPARATIVE ATTRIBUTE | FURTHER DEVELOP CEDAR HILLS CAPACITY | EXPORT TO OUT-OF-COUNTY LANDFILL | WASTE-TO-ENERGY FACILITY
Cost per Ton (2029$) | $41 | $55 | $136
Life Cycle Greenhouse Gas Emissions (EPA’s WARM Model) | (131,000) MTCO2e | (77,000) MTCO2e | 12,000 to 80,000 MTCO2e
Annual Greenhouse Gas Emissions (EPA’s eGGRT) | 95,000 MTCO2e/year | 95,000 MTCO2e/year | 1,200,000 MTCO2e/year
Recycling Rate | No Change | No Change | 2% Increase
Risks | SEPA, Permitting | Rail Capacity, Control | Siting, Sizing

## Slide 7
Title
Bullet
Points
Chart: MTCO2e
| Waste to Energy
King County Waste Composition | 80000
National Average Mixed MSW | -50000
Waste composition is extremely important when evaluating the impact of any disposal technology.
Waste To Energy GHG Emissions

## Slide 8
Siting & Permitting Pose
“Difficult to Quantify Risks”
Site requirements estimated at 40-55 acres
“Political acceptance and future regulations are two difficult-to-quantify risks". (ARCADIS 2019)
WTE permitting schedule “is based upon the assumption that there are no significant regulatory hurdles or public opposition to the project”. (ARCADIS 2019)
History of 1980s siting in Renton

## Slide 9
Conservative estimates are that 7% of the ash could be in demand by local markets. The remainder would be landfilled in a monofil cell.
Cedar Hills does not have a space designated for a monofil.
Out of county export of residual ash would be required.
WTE Doesn't Eliminate Landfilling

## Slide 10
Any alternative to Cedar Hills will be more expensive. WTE is not off the table – we are more informed and will continue to keep an eye on evolving technology.
We are not limited to either Landfilling or WTE. There are many other alternatives that should be considered as part of the solution.
We will collaborate across traditional boundaries to discover and desing our regional resource and waste management system. (ZWORP)
By 2025, we will upate our regional Comp Plan to guide our strategies to zero waste.
Key Take Away Messages

## Slide 11
Questions?

## Slide 12
King Street Center
201 South Jackson Street, Suite 701
Seattle, WA 98104-3855
206-477-4466
711 TTY Relay
your.kingcounty.gov/solidwaste