## Slide 1
PLA HSPF Watershed Toxic Model Calibration Results
Notes: We need to calibrate the model to minimize the simulated and observed differences by adjusting the toxic parameters so that the calibrated model can be used for decision-making, prediction, and etc.

## Slide 2: Green/Duwamish River Sub-Watersheds, and Estimated Load to LDW
USGS12113390
FL319
A315
A320
NC0322
Lake Young
Howard Hansen Dam (HHD)
Newaukum
Middle Green 1
Middle Green 2
Middle Green 3
Covington
Jenkins
Soos
Black River
Lower Green
Duwamish
KP319
PS317
FG319
Toxic Load to Lower Duwamish Waterway (LDW)
Toxic Load  Reach 604  LDW
Reference:
Lower Duwamish Waterway Air Deposition Scoping Study, Data Gaps Report. December, 2013.
20-year HSPF simulation order:
1) Jenkins  2) Covington  3) Soos  4) Newaukum  5) Middle Green 1  6) Middle Green 2  7) Middle Green 3  8) Lower Green  9) Black River  10) Duwamish
LDW-0309
R604
Notes: 20 year average, snapshot of data analyses.

## Slide 3: Statistical Calibration Targets for Reference
Model Component | Very Good | Good | Fair | Poor
Toxics | < 20% | 20 – 30% | 30 – 40% | > 40%
General calibration targets for HSPF toxic simulations (magnitude of Relative Average Error (RE, %)) (Donigian, 2000)
Reference:
Donigian, A. S., Jr. 2000. Lecture 19: Calibration and verification issues, Slide L19-22. HSPF training workshop handbook and CD. Presented and prepared for the U.S. EPA Office of Water and Office of Science and Technology, Washington, D.C.
where RE = relative average error in percent, Oi represents the time series observations and Pi is the time series of model predictions, n is the number of data pairs. The relative error is the ratio of the absolute mean error to the mean of the observations and is expressed as a percent (%).

## Slide 4: Calibration Method
Calibration Sequence
Flow rates
Water Quality
(setup)
HHD Dam
Tributaries & River
Hourly & Daily
Develop HHD Loads
Initial State
(conc. & mass)
Atmospheric Dep.
Groundwater
Variables
- define potency - adjust washoff
Particulate &
Soil
Dissolved &
Sorbed (conc.)
Adjust
Bed Sediments
(conc.)
Sensitivities
Notes: Both visual and statistics are used to evaluate the toxic concentration result. Also, we look at the total load to LDW.

## Slide 5: Calibration Table
LDW (Black + Lower Green)
Reach 604
Model Status
Notes: Duwamish – Hamm Creek, a lot of tributaries.
Upstream stations, tidal influenced.
1st round toxic calibration is complete. still rooms for the improvements. We found it necessary to go back to repeat the process.

## Slide 6: Whole water Total Arsenic (µg/L) – A315 (Lower Green)
A315: Mill Creek at the bridge at 68th Ave and South 261st Street
Total Arsenic
Arsenic Time Series
All data
Wet Season
Dry Season
Probability
Time Series
Cross Plot
Notes: Meaning of the plots

## Slide 7: Dissolved Arsenic (µg/L) – A315 (Lower Green)
Dissolved Arsenic
Arsenic Time Series
A315: Mill Creek at the bridge at 68th Ave and South 261st Street

## Slide 8: Revised Whole water Total Copper (µg/L) – A315 (Lower Green)
A315: Mill Creek at the bridge at 68th Ave and South 261st Street
Total Copper
Copper Time Series
Copper Time Series
Hard to fit
Notes: Scatter plots to five years.

## Slide 9: Whole water Total PCB (pg/L) to LDW – Reach 604
12113390
FL319
LDW-0309
Notes: Improve, start from a Table.

## Slide 10: Next
Further optimize model parameters by
  reconsidering the spatial difference
  double-checking the spatial pattern, and
  readjusting the spatial parameters
Continue adjust and/or modify
  sediment bed concentration
  adsorption/desorption rate
  partition coefficient
  groundwater concentration
Improve upstream toxic boundary condition at HH Dam, if applicable
Apply building age to the parameterization