## Slide 1: An Introduction to Instream Flows Science, Policy, and Impacts to Availability
April 3 2019
WRIA 10 Restoration and Enhancement Committee
Jim Pacheco
Instream Flow Biologist
Notes: I’ve been working on ISF science and policy since I started with Ecology in 2002.
Over the years, Washington State has become a national leader in the research and development of instream flows. Today I hope to give you an understanding of the what's, why’s, and how's of ISFs and their impact on water availability
Through the years I’ve conducted numerous ISF studies,
helped many watershed groups develop the instream flow component of their watershed plans,
developed the scientific rationale for several instream resource rules, and
Worked to improved the science behind our instream flow recommendations
Because much of my work involves technical discussions and negotiations with a lay audience,
I’ve found trust to be critically important.
To develop and maintain this trust,

## Slide 2: The Trout
Notes: I rely on the simple principal of speaking the trout,
the whole trout, and nothing but the trout.

## Slide 3: The Water Resources Program manages water and is responsible for developing and defending Instream Flows
Notes: The Water Resources Program manages water to meet the needs of people and the natural environment
One of our responsibilities is to develop and defend Instream Flows.

## Slide 4: What is an Instream Flow?
An instream flow (ISF) is a water right for the stream.
It has a priority date
  Water rights senior to the instream flow are unaffected but junior water rights can be regulated
It is not required to be met.
  Water rights e a right to use when available, not a guarantee that water will be available.
ISFs do not and cannot add more water to a stream
Notes: One of the tools used to manage the water is an instream flow.
Which is a very confusing term and is often misused, even by WR. For example, there is a huge difference between stream flow and ISF.
Stream flow is the volume of water in the stream at any moment
An instream flow is a water right for the stream
Like other water rights, it has a priority date, is based on beneficial use, and follows the seniority system set up in water law
This means that water rights senior to the instream flow are not affected, but water rights junior to the ISF can be regulated
Like other water rights, an ISF is not required to be met.
Water rights are a right to use when its available, not a guarantee that water will be available.
ISFs do not and cannot add more water to a stream.

## Slide 5: Why we need Instream Flows
Our thirst for water is often greater than nature’s ability to provide it, especially in the summer.
Lower stream flows contribute to a number of environmental concerns
Source USGS: Trends, 1950-2010
Notes: Washington’s ISF laws originated in 1969 and 1971, but concept of Instream Flows dates back at least 1949 where the Fisheries Code stated: (Chapter III, sec 46)
That a flow of water sufficient to support game fish and food fish populations be maintained at all times in the streams of this state.
But it took decades of increasing water withdrawals and lower stream flows for us to recognize and take action on one simple truth:
That our thirst for water is often greater than nature’s ability to provide it, especially in the summer.
For example, if that if we irrigated all the available acreage in central and eastern Washington, Idaho, and Montana, we could dry up the Columbia.
These lower stream flows contributed to a number of environmental concerns, including reduced fish populations.

## Slide 6: Why we need Instream Flows
About 75% of the state has at least one endangered or threatened salmon or trout species.
Low streamflows are just one of the reasons for this decline.
In the early 1970’s, Ecology started developing Instream Flow rules.
Notes: It’s a sad fact, but around 75% of the state has at least one endangered or threatened salmonid.
There are many factors contributing to this decline, commonly grouped into the four H’s; Habitat, Hatcheries, Harvest, and Hydro.
Low streamflows are just one of the habitat factors.
Because of these many factors, It’s taking a comprehensive approach to address this decline.
In the early 70’s Ecology began developing ISF rules to address the low flow factor and to protect and preserve instream resources.
What are Instream Resources? These are the are the animals, activities and social values that benefit from having enough water in the stream.
These include:

## Slide 7: Instream Resources: Fish & Wildlife
Notes: Fish and wildlife: It’s sad to say, but we have had to point out that fish do indeed need water and that dry streams or increasing the dry period in intermittent streams does not protect the resource. <CR>
Boating, Fishing, and other recreational activities : I don’t think dragging a kayak through the shallows is the experience most boaters are looking for <CR>.
Scenic or Aesthetic values, These are pictures of Shoshone Falls in Idaho and for many years, it was dry during the summer as all the water was diverted for power generation.
Now it has a 300 cfs instream flow;
During daylight hours; Between April 1 and Labor Day.
I know it sounds funny, but it protects and preserves aesthetic qualities when people are most likely to see it.
Other instream resources include Water Quality and Navigation. <CR>

## Slide 8: Instream Resources: Recreation such as Boating and Fishing
Notes: Recreation: Boating and Fishing

## Slide 9: Instream Resources: Scenic or Aesthetic Values
Notes: Scenic or Aesthetic Values

## Slide 10: Streamflows Fary
Hydrology 101
Streamflows Vary
Daily
Yearly
Seasonally
Notes: To help understand instream flows, we should have an understanding of stream hydrology and streamflow statistics.
Here is a hydrograph showing two different years of daily stream flow data on South Prairie Creek
This graph uses a normal or linear scale graph where each gridline represents the same interval, in this case the vertical interval is 500 cfs or cubic feet per second-that’s a measurement of the volume of water moving over time.
As you can see, streamflows vary…a lot.
They vary daily: In 2009, the January 6 streamflow was 1030 cfs. On January 6, the streamflow was 7510 cfs, over 6000 cfs higher in 1 day.
They vary yearly: In 2017, the January 8 streamflow was 125 cfs, but in 2009 we saw that the streamflow was 7510 cfs.
And they vary seasonally: This system has wet winters and springs and dry summers
With linear graphs it’s easy to see the large difference between stream flows, but low flows tend to squash together. For example, can anyone tell me what the lowest flow was in 2017?

## Slide 11: Logarithmic Scale
Hydrology 101
Logarithmic Scale
This is the same data shown in a different way
Log scales are used to show data with widely ranging values
Notes: This hydrograph shows the same two years of data, but it uses a logarithmic or Log scale where the major vertical intervals represents increasing orders of magnitude or factors of 10.
With this scale we can see that the lowest flow was in 2017 flow was around 30 cfs.
Log scales are useful for showing data with widely ranging data, so I commonly use a log scale to show streamflows

## Slide 12: Logarithmic Scale Cont.
Hydrology 101
Logarithmic Scale
69 years of data
Daily flows can vary by 2 orders of magnitude
Seasonal flows can vary by 3
Notes: This graph shows the same stream with all the daily stream flow data for 69 years of daily streamflow data
It is quite messy, but it shows us that within a few days, streamflow commonly varies 2 orders of magnitude.
Seasonally this stream varies by 2 orders of magnitude, but some of our streams can vary by 3.

## Slide 13: Exceedance Curves
Show the yearly and seasonal variability
Hydrology 101
Exceedance Curves
Without the Mess
Notes: Here is the same graph overlaid with a streamflow statistic called exceedance curves
The upper blue line represents the 10% exceedance flow.
Streamflows at this level are only exceeded 10% of time. Think of it as a rare wet day where it has been raining for a while, or when its raining really hard.
The bottom red line is the 90% exceedance flow.
Streamflows at this level are exceeded 90% of the time. When streamflows reach this level, it has been dry for a while.
In the summer, these would be drought conditions.
The dark blue line in the middle is the 50% exceedance flow. This is the same as the median.
<CR> By using 10-50-and 90% exceedance curves we can see most of the variability in a stream along with its seasonal pattern, without the mess

## Slide 14: Streamflow Patterns
A Rain dominated streamflow pattern tends to have the lowest summer flows and the longest low flow season
Hydrology 101
Streamflow
Patterns
Notes: Which is why I usually display stream flows using these exceedance curves.
In Washington, streams tend to follow one of three flow patterns
Deschutes River shows a Rain dominated pattern where streamflows are highest from winter and spring rains and decline rapidly as the rains stops.
Rain dominated systems tend to have the longest period of low flows and the highest seasonal flow differences.
The range of flows here are lower than usual for a rain-fed system with the summer flows being higher than expected for a basin this size.
This is caused in part by a large GW recharge component of the basin. The free flowing artesian wells and GW fed lakes (like Hicks Lake) are examples of GW influences in the lower basin.

## Slide 15: Streamflow Patterns Snow
A Snow dominated streamflow pattern
Note the lack of large November and December rain events
Hydrology 101
Streamflow
Patterns
Notes: The Wenatchee River is an example of a Snow dominated streamflow pattern
With a Snow dominated streamflow pattern there can be some rain in the winter, but most of the precipitation is stored as snow.
Streamflows get a large bump during the summer melt.

## Slide 16: Streamflow Patterns Mixed
A Mixed (Rain with Snow or Glacial melt) streamflow pattern have two bumps
Hydrology 101
Streamflow
Patterns
Notes: The Puyallup River has a mixed pattern with high streamflows in the winter from rain in the low lands and another in the spring and summer from melting snow and ice in the mountains.
Stream hydrographs will be an important tool for you to determine critical flow periods and the months where water could be available for storage or recharge projects so you should have them available when you have those discussions.
Now back to instream flows.

## Slide 17: Instream Resource Rule WRIA 10-1980
Jan 1-Feb 1 and May 1 to July 1: 95% Exceedance
Sept 15-Nov 1: 90% Exceedance
Notes: There have been roughly three phases of ISF development.
From 1973-1980, ISFs were determined by what was loosely called the hydrologic or stream rating method.
With this method, a stream was split into a high and a low flow period
The high flow period had the ISFs set at the 95% exceedance and the low flow period had an ISF between the 95 and 60% exceedance depending the stream’s rating
The Puyallup River, with a mixed pattern, had 2 high flow periods; January 1 to February 1 and May 1 to July 1, and the ISF, shown by the green line, was set at the 95% exceedance or 1400 cfs and 2000 cfs.
The low flow period was September 15 to November 1 and had the ISF set at the 90% exceedance or 1000 cfs
A straight line connected the different periods.
It was that simple…and was our least protective standard

## Slide 18: “Base Flow”, “Minimum Flow” What does it mean?
Definitions and consequences
Hydrology: streamflow from groundwater discharge
This hydrologic minimum is similar to drought conditions and does not provide much protection for the instream resource
Resource-Focused: streamflow needed to protect or preserve the resource
This usually leads to flows higher than the hydrologic minimum, but it provided a better level of protection
Notes: The legislature directed Ecology to develop instream flows in 1971, but did not define several key terms such as
Base flow and minimum flow
The definition you use is important because it could lead to very different ways of determining an instream flow.
For example, a base flow defined by hydrology would use the level of streamflow coming solely from groundwater.
This is relatively easy to measure, but since this hydrologic minimum can be similar to drought conditions, it does not provide much protection
On the other hand, A Resource-Focused definition would look at a streamflow that protects and preserves the instream resource.
This is harder to measure and it usually leads to ISFs higher than the hydrologic base, but it provided a better level of protection.

## Slide 19: Instream Resource Rules 1981-1985
Several models/methods were developed in the 1970s, but were not factors until this second phase.
The most common for ISF rules were the Toe-Width Method and PHABSIM model (Physical HABitat SIMulation)
Instream Resource Rules 1981-1985
Videos by Manu Esteve 2000
Notes: In the second phase of ISF development, biologists from WDFW and Ecology pushed for a more resource focused definition for ISFs.
There were several habitat based instream flow models/methods developed in the 1970s and used in Washington, but they were not used for ISFs until this second phase.
These include the Toe-Width which was the most commonly used method, and
PHABSIM which stands for Physical HABitat SIMulation.
This was typically used on the larger streams.

## Slide 20: Instream Resource Rule WRIA 1 - 1985
A hybrid between Resource and Hydrology based ISFs
Notes: Fishtrap Creek in WRIA 1 is an example of ISFs from this second phase.
Here the black line shows the recommend flows based on a Toe-Width study:
October-January: 58 cfs was preferred for Chinook spawning,
February-June 15: 52 cfs for Steelhead spawning, and
June 16-Septeptember: 12 cfs for Steelhead rearing.
The green line shows the negotiated instream flow.
They didn’t published rationale for this difference, but, ISFs in this phase were commonly limited to the 50% exceedance flow during the wet season and
up to the 40% exceedance during the dry season suggesting an unwritten hydrologic limit.
ISFs set during this period were usually higher and more protective than those set in the first phase

## Slide 21: Instream Resource Rules 1986-2000: The Dark Ages
Instream flow rule making moratorium for 15 years
Instream flow studies and fish habitat research continued
Many hydropower projects were conditioned with instream flows
Instream Resource Rules 1986-2000:
The Dark Ages
Notes: Then the dark ages fell and we has an ISF moratorium for 15 years
During this time, WDFW and Ecology continued to conducted Phabsim and toe-width studies all over the state.
They also continued their fish habitat research to improve the accuracy of the models
Even though we didn’t develop any ISF rules, we were able to set ISFs at hydroelectric projects through the State’s 401 water quality certificate.

## Slide 22: Instream Resource Rules 2000-2015
Ecology hired a second biologist and increased the size of WDFWs water team to implement RCW 90.82
Watershed plans were adopted resulting in 11 new instream flow rules
Instream Resource Rules 2000-2015
Notes: During the third phase of ISF protection hired a second biologist, increased the size of WDFWs water team, and started implementing RCW 90.82
During this time, we used the adopted watershed plans to develop or update 11 ISF rules
let’s look at how we develop a modern ISFs

## Slide 23: Key Instream Resources
Fish habitat is a key instream resource. The goal is to protect flows needed for:
Migration
Spawning
Rearing
Notes: ISFs are designed to protect instream resources. They all need to be considered when developing an ISF,
but we have the best quantitative tools for measuring fish habitat so we generally use fish as the key instream resource.
We have also found that if we protect fish habitat, the other instream resources are protected as well.
All Fish lifestages need adequate depth and velocity. For example, these migrating chum could more water to aid their migration.
But Spawning adults also need suitable gravel for building their redds (or nests),
And Rearing juveniles also need cover or places to hide from high velocities and/or predators.

## Slide 24: How Do We Develop an Instream Flow?
1) Habitat Study
2) Fish Periodicity
3) Stream Hydrology
Notes: To develop an ISF, we first need a study that relates fish habitat to stream flow.
Second, we need a Periodicity Chart. This comes from local biologists and tells us what fish species and lifestage are in the stream month by month, and
Third, we would like to have a long-term hydrograph of the stream.
For the Habitat Study, we continue to prefer either the Toe-Width method or a PHABSIM study.

## Slide 25: The Toe-Width Method Measuring stream width at the toe of the bank - the point where the stream bed meets the stream bank.
Notes: The toe-width method uses the width of the river measured at the toe of the bank, which is the point where the stream bed meets the stream bank.
When measured at pool tail-outs and riffles, and using the new protocols we published,
the widths are quite consistent and give more accurate estimate the ISF recommended by a PHABSIM study, but with much less effort.
This type of study is easy enough that all the key streams in an entire watershed can be measured in 1 to 3 days.
In fact, most of Washington’s ISF rules were developed using the Toe-Width method.

## Slide 26: PHABSIM
Measure around a thousand points data points - Our most detailed and site-specific instream flow method
The model predicts how depth and velocity changes with different stream flows
The model then compares these changes to the depths, velocities, and substrates preferred by different fish species.
Notes: PHABSIM is currently our gold standard for setting ISFs.
To conduct a Phabsim study, we first take hundreds of depth and velocity measurements at several different stream flows.
This is our most detailed and site specific ISF method and is much more time intensive.
The model takes all this data and predicts how depth and velocity conditions change over a wide range of stream flows.
Then it compares the conditions at different flows and compares it to the depth and velocity preferred by different fish species and lifestages.

## Slide 27: Results from a PHABSIM model
These curves show the amount of habitat available at each of the modeled stream flows.
Notes: Here are the results from a PHABSIM model from the EF Lewis showing the fish habitat to streamflow relationship.
In general, low flows are too shallow and slow and fish don’t like it.
High flows are too deep and fast and fish don’t like it.
At some varied stream flow, the stream produces the most fish habitat for each of the modeled species and life histories.
The highlighted portion of the table are the peak habitat values and the associated streamflows are used to develop a draft recommendations.
This type of model is considered reliable and defensible because it is quantitative and based on biological principals.
It is also quite popular. PHABSIM is used in 13 of the 17 western states and is the preferred method in 11 of them.

## Slide 28: Instream Resource Rule WRIA 27 - 2009
Instream Resource Rule WRIA 27 - 2009
Periodicity tells us what to protect
The habitat study tells where to set the ISF
Hydrology truth check the results.
Notes: Periodicity tells us when the various fish species are in the system and helps us focus on what to protect.
For Example, Chinook Salmon are spawning and incubation from October through February and the habitat study tells us 500 cfs provided the preferred streamflow.
Steelhead spawn March 1 through May and 460 cfs protects spawning.
Steelhead juveniles real year-round so all the other months get a rearing flow of 420 cfs.
Modern rules also use a hydrologic limit because the ISF should be “achievable”, but that was another undefined word.
Rare flow events can provide benefits to rearing fish populations, so we use the 10% exceedance as our hydrologic limit to habitat flows.
This has been our most protective ISF standard.
Under this ISF regime, new water users would have a reasonable chance of obtaining water from November through May
But how do ISFs affect uninterruptable water needed for new homes?

## Slide 29: WRIA 27/28 Availability-2009 rule
Stream No. of years the Avg. days per year
name ISF was not met ISF was not met
Kalama River 20/20 183
E Fork Lewis River 8/8 169
Washougal River 11/11 177
Burnt Bridge Creek 4/4 251
Notes: To answer this question, I looked at how often the ISF was not met in a watershed from a recent ISF rule using up to 20 years of daily streamflow data and a continuous 7-day not met threshold.
This means that the streamflow had to be below the ISF for at least 7 consecutive days before the ISF was considered “not met” for that year.
With today’s high standard, all the gaged streams in the WRIA had at least one 7 day event every year where the ISF was “not met” meaning that new uninterruptable water would not be available.
And then the polite and civil disagreements begin

## Slide 30: SEE!!! I told you the Instream Flow is Too High!!!
Fish don’t need that much water!
Notes: Mark Twain’s old adage that “whiskey's for drinking and water’s for fighting over”, is alive and well when dealing with instream flows.
We are frequently challenged with the claim that the ISF is too high,
And, that fish don’t need that much water!
HOWEVER, since 1935 research studies have consistently found a strong relationship between salmon abundance and streamflow.

## Slide 31: Fish vs Flow Research
Dave Seiler’s studies on Bingham Creek for 1980-1997 found more summer flow equals more coho smolts outmigrating the following spring.
Notes: The strongest relationship I’ve seen comes from Dave Seiler’s studies on Bingham Creek. He found that a higher summer flow resulted in more coho smolts out-migrating the following spring
The R^2 was 0.96. You don’t often see 0.96 as a biological response?
In general the research is showing that more flow means more fish.
However, if our critics are correct, simply using a lower ISF standard would solve the rural water problem, right?

## Slide 32: WRIA 1 Availability-1985 rule
Stream No. of years the Avg. days per year
name ISF was not met ISF was not met
Fishtrap Creek 20/20 209
Nooksack (RM 36.6) 19/20 154
Nooksack (RM 5.8) 20/20 142
MF Nooksack (RM5.0) 20/20 144
SF Nooksack (RM 14.8) 20/20 204
Skookum Creek 20/20 181
Notes: Here I used the same 7-day threshold analysis looking at availability under ISFs set during our 2nd phase of rule development .
Under this standard, we started using a resource focus for ISFs, but had hydrologic limits of 50% during the winter and about 40% during the summer.
Using this lower protective standard, ISFs were not met in almost every year, and for an average of 172 days.
So even with a lower standard, new uninterruptable water would not be available.

## Slide 33: WRIA 10 Availability-1980 rule
Stream No. of years the Avg. days per year
name ISF was not met ISF was not met
Puyallup River (RM 6.6) 7/20 46
Puyallup River (RM 12.2) 7/20 43
WRIA 22 - 1976
Chehalis River (RM 59.9) 15/20 43
Satsop River 17/20 72
Humptulips River 16/20 41
Notes: Finally, let look at availability on one of our first ISF rules.
This phase used our least protective standard that based ISFs on the 95% exceedance during high flow periods and between the 95 and 60% exceedance during the low flow period.
There were only two streams in WRIA 10 with the data needed so I added streams from WRIA 22, another rule from the first phase and results were quite stunning.
Even using our lowest standard, WRIA 10 ISFs were not met over a third of the time and over half the time in WRIA 22.

## Slide 34: WRIA 10 Rule - 1980
This Puyallup River hydrograph “shall be used for definition of instream flows on those days not specifically defined in WAC 173-510-3(2).
WRIA 10 Rule - 1980
Notes: Going back to the WRIA 10 rule, I noticed a few things you could fix to improve water management and provide options for future streamflow restoration projects.
This Puyallup River instream flow hydrograph “shall be used for definition of instream flows on those days not specifically defined in WAC 173-510-3(2).
When you plot all the ISF numbers, we see that someone at Ecology clearly made some mistakes.

## Slide 35: WRIA 10 Rule - 1980 Cont.
WRIA 10 rule has minor errors comparing the 2 Puyallup River IFS with the assigned graph, but the Carbon River has major errors.
WRIA 10 Rule - 1980
Notes: Here is the hydrograph showing the listed ISF in the rule and the ISFs from the appropriate graph.
The little dips or peaks on the Puyallup graphs are from rounding errors,
But the Carbon River clearly has the wrong number listed in the rule. This is an administrative error that could be addressed if you decide to update the rule.

## Slide 36: WRIA 10 Instream Resource Rule
WRIA 10 Instream Resource Rule
A Table of existing and new Stream Closures from the Rule
Year-round closures could impact potential water retiming projects
Notes: The WRIA 10 rule basically has year-round closures on all streams in the Basin.
This means that without a rule change, new potential water retiming projects could be prohibited

## Slide 37: Stream Closures in the WRIA 10 Rule Are they justified, or can they be seasonal?
Year-Round Closures
South Prairie Creek
Based on a Toe-Width study, there appears to be availability November 15-May 31
Notes: South Prairie Creek has a year-round closure, but it had high winter flows. Is a year-round closure justified?
Here we have a TW study that suggests winter and spring water may be available. You would need to negotiate with the interested parties, but it would be possible for this group to recommend changing to a seasonal closure based on water availability.

## Slide 38: Stream Closures in the WRIA 10 Rule Are they justified, or can they be seasonal?
Year-Round Closures
Boise Creek - A tributary to the White River
We would need a habitat study, but it could show winter and spring availability for water restoration projects
Notes: Boise Creek also has a year-round closure, but has high winter and spring flows. Is a year-round closure justified?
You would need a habitat study and negotiations with the interested parties, but it would be possible for this group to recommend changing to a seasonal closure based on water availability.

## Slide 39: Stream Closures in the WRIA 10 Rule Are they justified, or can they be seasonal?
Year-Round Closures
Kapowsin Creek - A tributary to the Puyallup River
We would need a habitat study, water could be available for water restoration projects
Notes: Kapowsin Creek is another example of a closed stream with high winter and spring flows.
Again we would need a habitat study and negotiations with the interested parties, but you recommend changing to a seasonal closure.

## Slide 40: Instream Resource Rule WRIA 10-1980
Jan 1-Feb 1 and May 1 to July 1: 95% Exceedance
Sept 15-Nov 1: 90% Exceedance
Notes: As a reminder, here is what the ISF looked like on the Puyallup
It was not very protective
Lower standards may make water available more often, but even they will not allow for new uninterruptable use.

## Slide 41: Instream Resource Rules 2016-20?? The Dark Ages Return
Swinomish v. Ecology (2013)-No impairment
Foster v. Ecology (2015)-No out of kind mitigation
Hirst v. Whatcom County (2016)-No building permit without water offset
Began another rule moratorium - Science marches on
Notes: This has been a legal wedge in the efforts to limit residential development resulting in several landmark WA supreme court decisions
Swinomish v. Ecology (2013) - No impairment even from reservations of water Ecology thought were in the public interest to provide
Foster v. Ecology (2015) - No out of kind mitiga ion – even it resulted in an improvement to instream resources
Hirst v. Whatcom County (2016)- No building permit without in-time in-place water offsets…
This effectively created a pseudo-building moratorium in some counties and others seemed just an easy lawsuit away from a similar condition
These cases also brought another rule moratorium, but science marches on. Last December, Ecology teamed up with WDFW and we published an update to the toe-width method

## Slide 42: In a Nutshell
Stream Flows vary; daily, yearly and seasonally, by 2-3 orders of magnitude
If we want to protect rare but productive stream flows, higher ISFs are needed, but even low standards would limit new homes
A 100 cfs withdrawal affect streams differently than a 0.00004 cfs in-house use, but water law treats them the same
Flexibility is clearly needed.
Notes: Stream Flows vary – on a given day, average streamflow can vary by two orders of magnitude but the instream flow is a single number.
If we want to protect the rare, but productive high flow years, a high level of protection is needed, reducing water availability.
But uninterruptable water wasn’t available even with a low levels of protection so reducing standards aren't the answer.
Large water uses such as municipal, industrial, and agriculture can have a measureable impact on streams, but in-house domestic use only has about a 25 gpd consumptive impact or .00004 cfs
With rare exceptions, this use would not would not affect the stream, but water law treats them the same.
Flexibility within water law is clearly needed

## Slide 43: Streamflow Restoration
Authorized new domestic wells in closed and impaired basins
Must offset 20 years of projected water use from new development
  In-time, in-subbasin is a priority, out-of-time & subbasin is allowed
    May include non-water projects.
  The water offset and non-water projects must result in a Net Ecological Benefit
Notes: There were many proposals, but after a two long years, Washington adopted RCW 9094, the Streamflow Restoration Act in January of 2018.
It gave us flexibility by authorizing new domestic wells in closed and impaired basins, but has 2 requirements.
First, the projected water use from 20 years of development must be offset somewhere in the basin.
In-time, in-subbasin are a priority, but out-of-time and out of subbasin projects are allowed
In addition to the offset projects, the plan may include non-water projects that improve instream resources
  Second, the projected water use and the combination of water offset and non-water or habitat projects must result in a Net Ecological Benefit – another undefined term we are struggling with

## Slide 44: There are many competing uses for water. RCW 90.94 lets us have strong ISF protection and the ability to provide water for new homes.
Calculating all the impacts and offsets will be difficult.
Our role is to provide technical assistance to help you be successful
Notes: There are many competing uses for water and conflicts are not always polite.
Ecology has tried to find ways to allow small uses within an ISF rule, but these have invalidated, or declared are too risky.
RCW 9094, the Streamflow Restoration Act is the new tool we have been given.
It let us have strong ISF protection with the flexibility of building new homes in the rural areas
Calculating all the impacts and offsets, and determining Net Ecological Benefit is going to be a difficult task. Our role is to provide watershed groups with the technical assistance they need to be successful…
for the benefit of People, Farms and Fish

## Slide 45: Thanks for listening Questions?
Jim Pacheco
Instream Flow Biologist
Water Resources Program
James.Pacheco@ecy.wa.gov
360-407-7458