## Slide 1
Growth Projections- Status Update
Initial growth projection (7/31/19) utilized methods and data provided by Kitsap, King, Mason, and Pierce counties.
Comments were compiled through August.
Comments are being reviewed and initial growth projection is being updated accordingly.
Option to accept initial growth projection (after updates per comments) or do growth projection scenarios.
  The intent of the scenarios is to evaluate the sensitivity of the growth projection methods, account for uncertainty, and facilitate selection of a projection, IF NECESSARY.
  Scenarios would require modifying the methods prescribed by the counties.

## Slide 2
Growth Projections- Initial Methods
Kitsap County Method
Identify 20-year growth projections from the Kitsap County Comprehensive Plan (the Comprehensive Plan is based on OFM medium population growth estimates, and conversion to dwelling units based on assumed people per household).
Allocate growth by subbasin based on proportion of historical building permits by subbasin from 2002–2019.
Conduct a buildable-lands analysis. Determine percentage of remaining buildout capacity within each subbasin that is within and outside of the waterline 200-foot buffer. Buildout capacity outside of a 200-foot waterline buffer is assumed to be served by permit-exempt well connections.
Multiply the growth for each subbasin (step 2) by the proportion of growth expected to be served by permit-exempt well connections (step 3).
Potential Changes to Methods
Change OFM estimate from medium to high (diverge from Comprehensive Plan) (change to step 1)
Use a different historical date range to spatially allocate growth among subbasins (change to step 2)
Base spatial allocation on historical permit-exempt well growth (change to step 2)
Change the waterline buffer from 200 feet to 1,000 feet (change to step 3)

## Slide 3
Growth Projections- Initial Methods
King County Method
Use historical building permit data (2000–2017) to project future growth
Define if each historical building permit used for growth projections is public or private (aka permit-exempt well) water service
Multiply the annual (projected) number of building permits per year by the percentage of permits using private water to determine a projected number of permit-exempt well connections per year to yield the annual rate of permit-exempt well connections
Multiply the rate of annual permit-exempt well connections by 20 for the estimated total of permit-exempt well connections over a 20-year period
Overlay subbasins to determine number of new permit-exempt well connections in each subbasin
Potential Changes to Methods
Use a different historical date range to develop 20-year growth projections to represent the high and low range of historical growth (change to step 1)
Base spatial allocation on the proportion of buildout capacity (available in late August)

## Slide 4
Growth Projections- Initial Methods
Mason County Method
Develop 20-year growth projections based on the Mason County Comprehensive Plan (the Comprehensive Plan is based on OFM medium population growth estimates, and conversion to dwelling units based on assumed people per dwelling unit)
Determine available land for single-family domestic units and determine proportion of buildout capacity by county urban growth areas (UGAs) and rural lands
Apply growth projections to buildable lands
Remove projected development unlikely to connect to a permit-exempt well (i.e., parcel is located within a water system service area; parcel is smaller than 1 acre)
Overlay subbasins to determine new permit-exempt connections in each subbasin
Potential Changes to Methods
Change OFM population growth projection from medium to high (change to step 1) (note that this would be a departure from the County’s Comprehensive Plan)
Base spatial allocation on historical growth (building permits) (change to step 2)
Adjust assumptions removing growth unlikely to rely on a permit-exempt well connection (change to step 4)

## Slide 5
Growth Projections- Initial Methods
Pierce County Method
Growth projection method: develop historical growth rates of permit-exempt wells for each subbasin using the Tacoma-Pierce County Health District (TPCHD) well database (1999–2018)
Forecast growth of future permit-exempt well connections for the 20-year planning horizon, based on the subbasin-specific historical growth rate
Allocate growth within each subbasin spatially, based upon buildable-lands analysis (i.e., parcel must be outside of UGA, not in a water and wastewater system boundary, not already built upon, or must have zoning category that allows for domestic use)
Potential Changes to Methods
Use a different historical date range to develop growth projections (1999–2008, 2009–2018). Consider using the maximum growth year (change to step 1).
Base spatial allocation on the proportion of buildout capacity (change to steps 1 and 2) (WRIA 12 only).
Allow for permit-exempt connections in water system service areas (based on historical permit-exempt well rates in water system service areas) and remove forestry land from analysis (very low likelihood of development) (change to step 3).

## Slide 6
Growth Projections- Initial Methods
Number of Permit-Exempt Wells Added between 2018 and 2038 |  |  |  |  | 
Subbasin | King | Pierce | Mason | Kitsap | Total
Bainbridge Island | -- | -- | -- | 489 | 489
Hood Canal | -- | -- | 950 | 1,133 | 2,083
McNeil Island, Anderson Island, Ketron Island | -- | 38 | -- | -- | 38
South Sound | -- | 940 | 244 | 714 | 1,898
Vashon-Maury Island | 368 | -- | -- | -- | 368
West Sound | -- | -- | -- | 2,286 | 2,286
Total | 368 | 978 | 1,194 | 4,622 | 7,162

## Slide 7
Growth Projections- Additional Scenarios
County | High | Low | Spatial Allocation
Kitsap | Change OFM estimate from medium to high | Change OFM estimate from medium to low | All based on proportional buildout capacity? All based on historical PE Well growth or building permits?
King | Change historical range of building permit data (2000 – 2008) | Change historical range of building permit data (2009 – 2017) | 
Mason | Change OFM estimate from medium to high | Change OFM estimate from medium to low | 
Pierce | Change historical range of well data (1999 – 2008) | Change historical range of building permit data (2009 – 2018) | 

## Slide 8
Growth Projections- Comments
County | Commenter | Document | Comment | Response
Mason | David Windom, Mason County Community Services Department | Growth Projection Tables | My planners are looking at the 244 well number vs. zoning. It's looking like 244 may be a tough squeeze. Given the character of the area with very expensive homes, we don't see that many going in over the time period. Can the consultant share their thoughts? | There's only 96 parcels available in the "South Sound" region for PE connections, given the zoning, parcels already built out and critical areas. Therefore, the extra (148 PE connections) overestimates growth in that area. Solutions may include re-allocating to the "Hood Canal" region or dispersing among the remainder of the county.
Mason | David Windom, Mason County Community Services Department | Growth Projection Tables | I had the planners looking over the work and comparing to the on the ground knowledge. We don't think the area of South Sound can support 244 new wells due to the steepness of slopes, zoning (mostly RR5 and RR10), and the fact that the shoreline is built out at this point. We think that 100 is pretty optimistic. | 
Kitsap, Pierce, Mason | Paul Pickett, Squaxin Island Tribe | Growth Projection Tables | Paul provided an analysis of growth projections, assumptions and buffers for worst case scenario based on HDR memo. | Evaluation during the WRIA 15 workgroup meeting
Kitsap, Pierce, Mason | Paul Pickett, Squaxin Island Tribe | Growth Projection Tables | The growth projection supporting data tables are very interesting. But I don’t see how the numbers in those tables add up to the numbers in the summary tables. There appears to be some missing steps. Could the consultants (Bob I assume) walk us through the tables and explain how they were turned into the values in the summary table? | Yes; offline or during the WRIA 15 workgroup meeting.
Kitsap, Pierce, Mason | Paul Pickett, Squaxin Island Tribe | Heat Maps | The heat maps are very interesting and helpful. I’d like some explanation of how the heat maps were developed. What are the colors telling us? To me they seem to highlight “hot spots”. But I’m wondering if the spatial averaging method loses some information. Is there another method that provides more spatial resolution? | The data contributing to the Mason Co and Pierce Co heat maps were developed using methods described in the appendices (in part). The heat mapsrepresent a point distribution, so the resolution was limited by the number of points. Also, we may want to avoid additional spatial resolution, because the nature of the projections is not meant to be parcel-specific.

## Slide 9
Growth Projections- Comments
County | Commenter | Document | Comment | Response
Pierce | Paul Pickett, Squaxin Island Tribe | Heat Maps | The Pierce heat maps raise some important questions regarding the “hot spots” for future PEWs. The number of PEWs and their concentration in certain areas suggests to me that we should divide the region into several subbasins. That was the intent of starting with “regions”, wasn’t it? This may be the opportunity to revisit the subbasin question. | Regarding the regions, yes, the plan was to revisit the region delineation once we saw the permit-exempt well projections and ideas on projects. We may touch on it in November or it may be better to wait until early 2020 once we see what projects are popping up.
Kitsap | Paul Pickett, Squaxin Island Tribe | Heat Maps | Could we get the Kitsap heat maps before the meeting Wednesday? I’d like to see where the growth in the South Sound “region” is projected. | David Nash provided heat maps
Mason | Paul Pickett, Squaxin Island Tribe | Mason County Map | Also, the map in the HDR memo for Mason County is in error. The area from Belfair east is not in the South Sound region – it’s in the Hood Canal region. Does this mapping error also indicate that the tables in the Growth Rate Table excel sheet are in error? 244 PEWs in Mason County’s portion of South Sound does not make sense given the tiny sliver is represents in the South Sound region – but it would make more sense as part of the Belfair area in the Hood Canal region. | The label was in error; the growth projection was correct, in terms of carrying out the prescribed methods; 244 PEWs exceeds the number of parcels available for PEW growth (96 parcels). Therefore, the difference should go to the
Kitsap, Pierce, Mason | Alison O'Sullivan, Suquamish Tribe Fisheries Department | Data tables | Why are PSRC growth projections not being used? Then portion out the allowed growth rate as per GMA (it is not clear what target growth is being looked at). | The project is estimating permit exempt well growth projections, not population growth. PSRC data does not predict permit exempt wells.
Kitsap, Pierce, Mason | Alison O'Sullivan, Suquamish Tribe Fisheries Department | Data tables | Why are new permits only being looked at? There are “vested” developments that are not being counted but still have potential new wells and would underestimate potential #. | The planning horizon is January 19, 2018 through January 18, 2038.
Kitsap | Alison O'Sullivan, Suquamish Tribe Fisheries Department | Kitsap County methodology | Is there something in Kitsap County code that requires hookup to PUD if they are within 200’? I don’t believe there is so this assumption would not be accurate and would underestimate potential #. | From David Nash, "We used the 200 feet from a waterline variable as it was discussed in one of our meetings. While the PUD has an “obligation” to serve any parcel within ¼ mile of a 4” or greater water main, I think the argument was that not everyone wanted public water. So those that bought land near roads would want more services than those who owned land further out in the rural areas. Also we don’t have all the data County-wide for waterlines (it seems many of the smaller provider are unable to create spatial data), so we are likely currently over-estimating PEWs."

## Slide 10
Growth Projections- Comments
County | Commenter | Document | Comment | Response
Kitsap | Samuel J. Phillips | Memo | I would like to see a discussion of the land capacity analysis (Kitsap County). Is this the same as buildable lands analysis? I am aware this is required by GMA but it would be helpful to explain how it is done. | From David Nash, "Remaining Buildout Capacity / Rural Growth Target – Both of these ideas relate to just going for buildout in my opinion."
Kitsap | Samuel J. Phillips | Memo | Appendix A lists WRIA 14 as including Kitsap County. I believe this is an error. | Commenter is correct error will be updated
Kitsap, Pierce, Mason | Samuel J. Phillips | Memo | The decision tree provided to County meeting participants should be included in Appendix A or more clearly referenced in the document. | The decision tree provided to County meeting participants was just an initial example for developing methodologies. Each County, if they chose to participate, developed methodologies of their own. The July 31, 2019 Growth Projections memo did not include a Kitsap Co decision tree, because it had not yet been developed by Kitsap Co. Included in the memo, however, as Appendix B and D, are flow carts for Pierce and Mason Counties.
Kitsap, Pierce, Mason | Samuel J. Phillips | Memo | The memo should include a discussion of how health district and water district data is used. | Kitsap County did not use health district or water district data except for the waterline data housed by KPUD. This is described in the memo.
Kitsap, Pierce, Mason | Samuel J. Phillips | Memo | Do I recall that there is a certain density of individual wells which would reach a threshold of Group B water system? Under what conditions do Group B systems consolidate? | Group B systems serve more than a single home. They serve fewer than 15 service connections and fewer than 25 people per day.